## Slide 1
Phase D-2 Feature Extraction Pipeline
How one spectrum is converted into 38 routing features
1
Input
R_total(λ)
ΔR_total(λ)
reference spectrum
+
case spectrum
Windowed energy features
Input: ΔR_total
Core: front / transition / rear windows
Output: front_rms, rear_rms,
front/rear ratio
Rear-window shift features
Input: rear-window R_total
Core: reference vs case,
best alignment
Output: best shift, explained fraction,
residual
Rear-window spectral features
Input: rear-window signal
Core: uniform 1/λ grid +
frequency analysis
Output: dominant freq, bandwidth,
sideband, complexity
Wavelet features
Input: ΔR_total
Core: localized scale-space
decomposition
Output: front / transition / rear
energy + entropy
Template similarity features
Input: ΔR_total
Core: compare against family mean
templates
Output: thickness / front roughness /
rear roughness / front gap /
rear gap similarity
→
38 quantitative features
window amplitudes
ratios
shift metrics
rear spectral metrics
wavelet metrics
template-similarity metrics
→
PCA / UMAP visualization
low-dimensional map for quick
family separation
automatic routing
choose the likely defect family
before fitting
family-specific full-spectrum fitting
send the routed case into the
matching full-spectrum fitter
→
→
→

## Slide 2
Phase D-2 Feature Groups Overview
Five complementary feature sources for defect routing
2
Windowed energy features
Input
ΔR_total(λ)
Output
front_rms, rear_rms,
front/rear ratio
Question answered
Where does the change mainly live?
Rear-window shift features
Input
rear-window R_total(λ)
Output
best shift, explained fraction,
residual
Question answered
Does it behave like thickness shift?
Rear-window spectral features
Input
rear aligned residual
Output
dominant freq, bandwidth,
sideband, complexity
Question answered
Is there extra rear-window complexity?
Wavelet features
Input
ΔR_total(λ)
Output
front/transition/rear energy,
entropy, peak scale
Question answered
Where is the change concentrated,
and is it locally reconstructed?
Template similarity features
Input
ΔR_total(λ) vs family templates
Output
thickness / front roughness /
rear roughness / front gap /
rear gap similarity
Question answered
Which defect family does it look like overall?
Summary route
5 groups
38 quantitative features
routing / embedding /
family-specific fitting
→
→
→

## Slide 3
Why not use raw spectra directly?
Route first, then fit the full spectrum with the matching family-specific model
3
Directly use raw spectra
Use feature extraction first
front
transition
rear
Chart: 
Chart: 
high-dimensional
hard to explain
noise-sensitive
hard to route physically
5 feature groups
window energy
rear shift
rear spectrum
wavelet
template similarity
38 features
compact numbers
with physical meaning
routing
choose the likely family
before full-spectrum fit
→
→
lower-dimensional
physically interpretable
good for classify-then-fit
better for automatic routing
feature extraction is used for routing, not for replacing full-spectrum fitting